## Slide 1: UNDER THE HOOD
VM
CSRX1
Left VN
10.10.10.0/24
left-ubuntu-cs
right-ubuntu-cs
Right VN
10.20.20.0/24
.2
.1
.2
.1
Notes: Service Template
Service templates are always configured in the scope of a domain, and the templates can be used on all projects within a domain. A template can be used to launch multiple service instances in different projects within a domain.
The following are the parameters to be configured for a service template:
Service template name
Domain name
Service mode
  Transparent
  In-Network
  In-Network NAT
Image name (for virtual service)
  If the service is a virtual service, then the name of the image to be used must be included in the service template. In an OpenStack setup, the image must be added to the setup by using Glance.
Interface list
  Ordered list of interfaces---this determines the order in which Interfaces will be created on the service instance.
  Most of the service templates will have management, left, and right interfaces. For service instances requiring more interfaces, “other” interfaces can be added to the interface List.
  Shared IP attribute, per interface
  Static routes enabled attribute, per interface
Advanced options​
  Service scaling---use this attribute to enable a service instance to have more than one instance of the service instance virtual machine.
  Flavor---assign an OpenStack flavor to be used while launching the service instance. Flavors are defined in OpenStack Nova with attributes such as assignments of CPU cores, memory, and disk space.
Service Instance
A service instance is always maintained within the scope of a project. A service instance is launched using a specified service template from the domain to which the project belongs.
The following are the parameters to be configured for a service instance:
Service instance name
Project name
Service template name
Number of virtual machines that will be spawned
  Enable service scaling in the service template for multiple virtual machines
Ordered virtual network list
  Interfaces listed in the order specified in the service template
  Identify virtual network for each interface
  Assign static routes for virtual networks that have static route enabled in the service template for their interface
    Traffic that matches an assigned static route is directed to the service instance on the interface created for the corresponding virtual network
Service Policy
The following are the parameters to be configured for a service policy:
Policy name
Source network name
Destination network name
Other policy match conditions, for example direction and source and destination ports
Policy configured in “routed/in-network” or “bridged/” mode
An action type called apply_service is used:
  Example: 'apply_service’: [DomainName:ProjectName:ServiceInstanceName]

## Slide 2: UNDER THE HOOD
VRF
left:left
VRF
left:service-SI1-left
VRF
right:service-SI1-right
pt_svm1
VRF
left:service-SI2-left
VRF
right:service-SI2-right
pt_svm2
VRF
right:right
-right
3.3.3.4
left
2.2.2.5
right
3.3.3.5
left
2.2.2.4
VM
2.2.2.3
tapX
VRF ASSIGN ACL triggers lookup in Auxiliary VRF
VM
VM
Notes: Service Template
Service templates are always configured in the scope of a domain, and the templates can be used on all projects within a domain. A template can be used to launch multiple service instances in different projects within a domain.
The following are the parameters to be configured for a service template:
Service template name
Domain name
Service mode
  Transparent
  In-Network
  In-Network NAT
Image name (for virtual service)
  If the service is a virtual service, then the name of the image to be used must be included in the service template. In an OpenStack setup, the image must be added to the setup by using Glance.
Interface list
  Ordered list of interfaces---this determines the order in which Interfaces will be created on the service instance.
  Most of the service templates will have management, left, and right interfaces. For service instances requiring more interfaces, “other” interfaces can be added to the interface List.
  Shared IP attribute, per interface
  Static routes enabled attribute, per interface
Advanced options​
  Service scaling---use this attribute to enable a service instance to have more than one instance of the service instance virtual machine.
  Flavor---assign an OpenStack flavor to be used while launching the service instance. Flavors are defined in OpenStack Nova with attributes such as assignments of CPU cores, memory, and disk space.
Service Instance
A service instance is always maintained within the scope of a project. A service instance is launched using a specified service template from the domain to which the project belongs.
The following are the parameters to be configured for a service instance:
Service instance name
Project name
Service template name
Number of virtual machines that will be spawned
  Enable service scaling in the service template for multiple virtual machines
Ordered virtual network list
  Interfaces listed in the order specified in the service template
  Identify virtual network for each interface
  Assign static routes for virtual networks that have static route enabled in the service template for their interface
    Traffic that matches an assigned static route is directed to the service instance on the interface created for the corresponding virtual network
Service Policy
The following are the parameters to be configured for a service policy:
Policy name
Source network name
Destination network name
Other policy match conditions, for example direction and source and destination ports
Policy configured in “routed/in-network” or “bridged/” mode
An action type called apply_service is used:
  Example: 'apply_service’: [DomainName:ProjectName:ServiceInstanceName]

## Slide 3: UNDER THE HOOD
VM
CSRX1
Left VN
10.10.10.0/24
Ubuntu-left-CS
Ubuntu-right-CS
Right VN
10.10.10.0/24
.2
.1
.1
.2
.1
Notes: Service Template
Service templates are always configured in the scope of a domain, and the templates can be used on all projects within a domain. A template can be used to launch multiple service instances in different projects within a domain.
The following are the parameters to be configured for a service template:
Service template name
Domain name
Service mode
  Transparent
  In-Network
  In-Network NAT
Image name (for virtual service)
  If the service is a virtual service, then the name of the image to be used must be included in the service template. In an OpenStack setup, the image must be added to the setup by using Glance.
Interface list
  Ordered list of interfaces---this determines the order in which Interfaces will be created on the service instance.
  Most of the service templates will have management, left, and right interfaces. For service instances requiring more interfaces, “other” interfaces can be added to the interface List.
  Shared IP attribute, per interface
  Static routes enabled attribute, per interface
Advanced options​
  Service scaling---use this attribute to enable a service instance to have more than one instance of the service instance virtual machine.
  Flavor---assign an OpenStack flavor to be used while launching the service instance. Flavors are defined in OpenStack Nova with attributes such as assignments of CPU cores, memory, and disk space.
Service Instance
A service instance is always maintained within the scope of a project. A service instance is launched using a specified service template from the domain to which the project belongs.
The following are the parameters to be configured for a service instance:
Service instance name
Project name
Service template name
Number of virtual machines that will be spawned
  Enable service scaling in the service template for multiple virtual machines
Ordered virtual network list
  Interfaces listed in the order specified in the service template
  Identify virtual network for each interface
  Assign static routes for virtual networks that have static route enabled in the service template for their interface
    Traffic that matches an assigned static route is directed to the service instance on the interface created for the corresponding virtual network
Service Policy
The following are the parameters to be configured for a service policy:
Policy name
Source network name
Destination network name
Other policy match conditions, for example direction and source and destination ports
Policy configured in “routed/in-network” or “bridged/” mode
An action type called apply_service is used:
  Example: 'apply_service’: [DomainName:ProjectName:ServiceInstanceName]

## Slide 4: UNDER THE HOOD
NO ACL at interfaces located at the “outside of the Service Chain”
pt_svm1
left
2.2.2.4
VM
tap8f345fc4-c1
Notes: Service Template
Service templates are always configured in the scope of a domain, and the templates can be used on all projects within a domain. A template can be used to launch multiple service instances in different projects within a domain.
The following are the parameters to be configured for a service template:
Service template name
Domain name
Service mode
  Transparent
  In-Network
  In-Network NAT
Image name (for virtual service)
  If the service is a virtual service, then the name of the image to be used must be included in the service template. In an OpenStack setup, the image must be added to the setup by using Glance.
Interface list
  Ordered list of interfaces---this determines the order in which Interfaces will be created on the service instance.
  Most of the service templates will have management, left, and right interfaces. For service instances requiring more interfaces, “other” interfaces can be added to the interface List.
  Shared IP attribute, per interface
  Static routes enabled attribute, per interface
Advanced options​
  Service scaling---use this attribute to enable a service instance to have more than one instance of the service instance virtual machine.
  Flavor---assign an OpenStack flavor to be used while launching the service instance. Flavors are defined in OpenStack Nova with attributes such as assignments of CPU cores, memory, and disk space.
Service Instance
A service instance is always maintained within the scope of a project. A service instance is launched using a specified service template from the domain to which the project belongs.
The following are the parameters to be configured for a service instance:
Service instance name
Project name
Service template name
Number of virtual machines that will be spawned
  Enable service scaling in the service template for multiple virtual machines
Ordered virtual network list
  Interfaces listed in the order specified in the service template
  Identify virtual network for each interface
  Assign static routes for virtual networks that have static route enabled in the service template for their interface
    Traffic that matches an assigned static route is directed to the service instance on the interface created for the corresponding virtual network
Service Policy
The following are the parameters to be configured for a service policy:
Policy name
Source network name
Destination network name
Other policy match conditions, for example direction and source and destination ports
Policy configured in “routed/in-network” or “bridged/” mode
An action type called apply_service is used:
  Example: 'apply_service’: [DomainName:ProjectName:ServiceInstanceName]

## Slide 5: UNDER THE HOOD
VM
CSRX1
Left VN
10.10.10.0/24
left-ubuntu-cs
right-ubuntu-cs
Eth1 Vif 0/6 tapeth1-7d8e06
Eth0 ge-0/0/0 Vif 0/9 tapeth2-844f1c
Eth1 ge-0/0/1 Vif 0/8 tapeth1-844f1c
Eth1 Vif 0/4 tapeth1-89a4e2
Right VN
10.20.20.0/24
.2
.1
.1
.2
.1
Notes: Service Template
Service templates are always configured in the scope of a domain, and the templates can be used on all projects within a domain. A template can be used to launch multiple service instances in different projects within a domain.
The following are the parameters to be configured for a service template:
Service template name
Domain name
Service mode
  Transparent
  In-Network
  In-Network NAT
Image name (for virtual service)
  If the service is a virtual service, then the name of the image to be used must be included in the service template. In an OpenStack setup, the image must be added to the setup by using Glance.
Interface list
  Ordered list of interfaces---this determines the order in which Interfaces will be created on the service instance.
  Most of the service templates will have management, left, and right interfaces. For service instances requiring more interfaces, “other” interfaces can be added to the interface List.
  Shared IP attribute, per interface
  Static routes enabled attribute, per interface
Advanced options​
  Service scaling---use this attribute to enable a service instance to have more than one instance of the service instance virtual machine.
  Flavor---assign an OpenStack flavor to be used while launching the service instance. Flavors are defined in OpenStack Nova with attributes such as assignments of CPU cores, memory, and disk space.
Service Instance
A service instance is always maintained within the scope of a project. A service instance is launched using a specified service template from the domain to which the project belongs.
The following are the parameters to be configured for a service instance:
Service instance name
Project name
Service template name
Number of virtual machines that will be spawned
  Enable service scaling in the service template for multiple virtual machines
Ordered virtual network list
  Interfaces listed in the order specified in the service template
  Identify virtual network for each interface
  Assign static routes for virtual networks that have static route enabled in the service template for their interface
    Traffic that matches an assigned static route is directed to the service instance on the interface created for the corresponding virtual network
Service Policy
The following are the parameters to be configured for a service policy:
Policy name
Source network name
Destination network name
Other policy match conditions, for example direction and source and destination ports
Policy configured in “routed/in-network” or “bridged/” mode
An action type called apply_service is used:
  Example: 'apply_service’: [DomainName:ProjectName:ServiceInstanceName]